## Slide 1
M2FS: The Michigan/Magellan Fiber
System: Data Reduction Overview

## Slide 2
Data are defined by:
Field — The set of targets observed in a
single observation/set of exposures.
Plate — The physical plate on which the
field is drilled.
Configuration — The full set of instrument
parameters that are used to carry out an
observation.
Setup — The full combination of field, plate,
and configuration used for a specific set of
observations.
M2FS: Terminology

## Slide 3
Configurations are defined by:
M2FS: Configurations
MSpec Side — B or R spectrograph.
Resolution — HiRes (Echelle + cross-disperer),
or LoRes (Standard/Echellette grating)
Grating Angles — El/Az (HiRes) or El (LoRes)
Blocking Filters — Isolate orders/BK7 in LoRes
Focus — B/R separate; depends slightly on
temperature.
Fiber Slits — Wide open to 45-microns; 8 pos.
CCD binning — Somewhat complicated, but
many options available; depend on amplifiers.
Readout Details — Speed; full/subraster.

## Slide 4
M2FS: Basics
Users select
configuration
variables via
instrument GUI.
Parameters can
be saved and
read from files.

## Slide 5
Red Side
Blue Side
Identical Channels; names are relics.
CCDs

## Slide 6
Echelle
Cam/Coll
xDisp Prism
M2FS Optical Layout: Theory/HiRes

## Slide 7
Grating
Cam/Coll
M2FS Optical Layout: Theory/LoRes

## Slide 8
Through commissioning (Aug 2013) and
two science runs (Nov 2013 and Feb 2014),
we now have 15 configurations defined:
Config 1 — Mgb filter; HiRes; 2x2; 180 mic slit;
grating angles.
Config 5b — Hot Jupiter filter; HiRes; 1x1; 45
mic slit; grating angles.
Config 9 — BK-7; 3700-5700A; LoRes; 2x2; 180
mic slit; grating angle.
Config 12 — Halpha/Li filter; HiRes; 1x2; 75 mic
slit; grating angles.
M2FS: Configurations

## Slide 9
Data logs (active) — Primary source of
information for images. IMAGE HEADERS
MAY NOT ALWAYS BE RELIABLE.
Data repository (active) — Available at
https://m2fs.astro.lsa.umich.edu/data/
(m2fs/m2fsdata)
Configuration parameter files — Saved at
the telescope; available if/as needed.
Data reduction scripts (not active) — TBD
M2FS: Resources to Users. I.

## Slide 10
Data format — Single extension FITS.
Multi-extension possible if demand is high.
Amplifiers — Currently support 1, 2 or 4-amp, readouts. At telescope, files are saved as
fNNNNcM.fits
where f=r,b, N=frame number, M=amp.
Data Directories — Standard practice is to sort by ut date: /utYYYYMMDD
Example — /feb2014/ut20140218/b0198c2.fits
M2FS: Data Characteristics. I.

## Slide 11
TCS Information — Telescope position, time of observation, orientation of dome, etc. RELIABLE.
Instrument Status — Environment temps, CCD temps, CCD readout details, configuration parameters, etc. RELIABLE.
Field/Plate Information — Name of plate, name of target field, full fiber cross indexing and information with target ids. NOT YET RELIABLE. Even when information is properly entered, fiber status may be wrong. Always check log.
M2FS: Data Headers

## Slide 12
Exposure info
CCD sampling
Slit assignments
System temps
Fiber mapping
M2FS: Data Headers

## Slide 13
M2FS: Fiber IDs
Each group of 16 fibers represents a ‘cassette’ or ‘tetris’.
The B and R side CCDs have different mappings of cassette/tetris and fiber numbers.
Fibers designated as SC-FF where S=‘side’ (R or B), C=Cassette #, FF=Fiber # in cassette (2 digit)

## Slide 14
M2FS: Fiber IDs RED SIDE
8
7
6
5
4
3
2
1
Cassette Number
1
16
A = Aperture #
Runs from 1  128, bot to top
C = Cassette #
C = int{(A-1)/16} + 1
FF = Fiber # within cassette
FF = A – (C-1)*16
(0,0)
CCD Y axis 
CCD x axis 
A=1
A=128

## Slide 15
M2FS: Fiber IDs BLUE SIDE
1
2
3
4
5
6
7
8
Cassette Number
1
16
A = Aperture #
Runs from 1  128, bot to top
C = Cassette #
C = 8 - int{(A-1)/16}
FF = Fiber # within cassette
FF = A – (8-C)*16
(0,0)
CCD Y axis 
CCD x axis 
A=1
A=128

## Slide 16
‘Fiber Maps’ — Available for all configurations for a given run and specified in logs. Consist of daytime images with all fibers plugged for given configuration. Used to define extraction para-meters. Multiple maps for multi-order config-urations. Part of data archive.
Plate Files — Separate lists for plates that detail all actual targets observed. Available on request. To be added to archive.
Calibration Data — Typically obtain appropriate arcs, associated quartz exposures, bias sequences, twilights as standard part of observations. In data archive.
M2FS: Resources to Users. II.

## Slide 17
Arc Finding Charts — Available on request for some orders. On request and to be supplemen-ted by users. Also MIKE ThAr atlas can be of use. LoRes atlases not available yet.
M2FS: Resources to Users. II.

## Slide 18
2x2 binning; HiRes; Single order per target.
M2FS: Data Characteristics. II.

## Slide 19
2x2 binning; LoRes (always single order per target).
M2FS: Data Characteristics. II.

## Slide 20
1x2 binning; HiRes; Four orders per target.
M2FS: Data Characteristics. II.

## Slide 21
IRAF based processes and Python routines have been developed by MM and JB
Simple command lists available for one-order, HiRes configurations (Mgb and CaT) from MM. Actual IRAF scripts under development. User respository for appropriate software to be developed as demand/availability dictate.
Limited documentation.
Examples here are all IRAF-based and are meant to illustrate key steps.
M2FS: Data Reduction: Overview

## Slide 22
Process raw images — Line overscan correction (ccdproc).
M2FS: Data Reduction: Overview

## Slide 23
Pack images — As needed depending on amplifier/binning choices. Results in single 2-D images with c1 header. (imcreate, imcopy)
M2FS: Data Reduction: Overview

## Slide 24
Scattered light correction — As desired. Scattered light depends on spectrograph, and distribution of target brightnesses. Best practices still in development. (imsurfit)
M2FS: Data Reduction: Overview

## Slide 25
Tracing orders — (1) Trace appropriate fiber maps for all N fibers for given configuration. (2) Apply trace to data directly or using ‘local’ quartz images as desired. (3) Apply to arcs and any other calibration data/standards. (apall)
M2FS: Data Reduction: Overview

## Slide 26
Identify arc lines — Determine pix-lambda transformation. (identify, reidentify)
M2FS: Data Reduction: Overview
HiRes rms ~ 100-300 m/s; LoRes ~ 1 km/s

## Slide 27
Dispersion correct data — Apply dispersion cor-rection to data as desired. Can either rebin data or simply place dispersion info in image headers for each fiber/aperture. (refspec, dispcor)
M2FS: Data Reduction: Overview

## Slide 28
Fiber corrections/Sky Subtraction — Remove fiber throughput variations. Remove average sky background
M2FS: Data Reduction: Overview

## Slide 29
Good velocity precision — Achieving 2-1% of resolution element at even low S/N
Flat fielding — Details still to be worked out
Web pages — Volunteers would be welcome!
At your service for help, advice, additional data as needed.
M2FS: Data Reduction: Comments

## Slide 30
M2FS: Data Reduction:
Random Samples of
Preliminary Results

## Slide 32
Fornax
Dwarf Galaxy
Dist = 220 kpc
HiRes Spectra
Individual Stars
400 stars/4 hrs

## Slide 33
Z ~ 0.36
Abell 267
Galaxy Cluster
z = 0.19
LoRes Spectra
Individual Galaxies
1.5 hrs
Z ~ 0.57

## Slide 34
9-10 Solid
Members